## Slide 1
6.888: Wireless Communications Systems
Lecture 1: Introduction
Dina Katabi

## Slide 2: General Information
Staff
  Lecturer: Dina Katabi, dk@mit.edu
  TA: Haitham Hassanieh, haithamh@mit.edu
Material (new class)
  Mainly research papers
  Your notes (each student will be a scribe for one lecture)
Prerequisites
  6.02 and 6.033
  Basic math: probability, Fourier, Dijkstra’s shortest path alg., …
  Matlab and C programming
Grading
  Research Project 50%
    Proposal, status report, presentation, final report
  Weakly Labs + Mini Assignments + Scribe notes – 50%

## Slide 3: Fundamental Architectural Change
Traditional Approach
New Approach
Optimize within isolated layers
HW and Radios
Comms. and Coding
Network & Apps
Optimize across the layers
HW and Radios
Comms. and Coding
Network and Apps
Cross-Layer Designs
Disruptive gains are unlikely
Major opportunities!

## Slide 4
10x Higher Data Rates

## Slide 5
The FCC projects that the US will face a spectrum shortfall in 2013.
Looming Wireless Capacity Crunch
The iPhone 4 demo failed due to wireless congestion.
Jobs’s reaction: “If you want to see the demos, shut off your laptops, turn off all these MiFi base stations, and put them on the floor, please.”

## Slide 6
MegaMIMO
Alleviates the capacity crunch by transmitting more bits per unit of spectrum

## Slide 7
Access Point 1
Access Point 2
Today’s Wireless Networks
Ethernet
Access Point 3
User 2
User 3
User 1
Today, Access Points Can’t Transmit Together in the Same Channel

## Slide 8
Access Point 1
Access Point 2
Today’s Wireless Networks
Ethernet
Access Point 3
User 2
User 3
User 1
Interference!
Today, Access Points Can’t Transmit Together in the Same Channel

## Slide 9
Access Point 1
Access Point 2
MegaMIMO
Ethernet
Access Point 3
Access Points Can Transmit Simultaneously in the Same Channel
Interference:
d2+d3≈0
Data: d1 survives
Interference: d1+d3≈0
Data: d2 survives
Interference: d1+d2≈0
Data: d3 survives
User 2
User 3
User 1

## Slide 10
User 1
Ethernet
AP1
User 2
AP2
User 3
AP3
User 10
AP10
                …
                …
Access Points act as a huge distributed MIMO transmitter with sum of antennas
10 Access Points  10x Higher Throughput
MegaMIMO = Distributed MIMO

## Slide 11: Testbed of Software Radios
Dense Conference Room Like Deployment

## Slide 12: Results from Prototype
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
MegaMIMO | 23.11 | 46.27 | 70.752 | 95.428 | 117.257 | 141.066 | 167.328 | 186.176 | 211.329 | 236.52
802.11 | 23.099 | 23.584 | 23.934 | 23.996 | 23.93 | 24 | 23.996 | 23.936 | 24.003 | 24
MegaMIMO
802.11
Total Throughput [Mb/s]
10x
10x throughput gain over existing Wi-Fi
Number of Access Points on Same Channel

## Slide 13: OpenRF (uses existing 802.11 cards)
Manages wireless interference
  Interference nulling, interference alignment, and beamforming
Self-configures MIMO techniques to benefit any network scenario
  Admins do not need to understand MIMO processing

## Slide 14: OpenRF’s Goals
AP-2
Bob
AP-1
Ethernet
Controls Access Points to apply PHY techniques
OpenRF
OpenRF
Alice
Notes: Let’s first understand what OpenRF aims to achieve in a wireless network.
We consider a simple example where we have two access points : AP-1 and AP-2 connected by a wired backbone.
Let’s say that the APs serve two clients Alice and Bob.
Essentially, OpenRF aims to control downlink traffic from APs to clients.
In other words, it provides a software layer that controls each Access Point in the network to apply PHY techniques.
The clients however are independent devices that we do not coordinate or control.

## Slide 15: OpenRF’s Goals
AP-2
AP-1
Ethernet
OpenRF
OpenRF
6 Mbps
time
Alice
Alice
Alice
Alice
Alice
Bob
Notes: Now let’s suppose Alice decides to start watching a High-Definition Youtube video.
Let’s say AP-1 sends packets to Alice at 6 Mbps, which is just about enough for good quality.
Now suppose Bob decides to watch a video as well!
Unfortunately, the wireless medium is shared …

## Slide 16: OpenRF’s Goals
Ethernet
time
Alice
Bob
Alice
Bob
Alice
Bob
Buffering…
Buffering…
AP-2
AP-1
OpenRF
OpenRF
3 Mbps
3 Mbps
Notes: … So, Alice and Bob are forced to take turns on the medium,
Thus, they only get half their earlier share, that is 3 Mbps each.
And this deteriorates the quality of service for both users.

## Slide 17: OpenRF’s Goals
Ethernet
“Interference Nulling”
Alice
Bob
null
null
AP-1
OpenRF
AP-2
OpenRF
3 Mbps
3 Mbps
Buffering…
Buffering…
Notes: To tackle this problem, OpenRF leverages a technique called interference nulling.
Essentially, AP-2 can leverage its multiple antennas to cancel any interference at Alice.
Similarly AP-1 cancels interference at Bob.

## Slide 18: OpenRF’s Goals
Ethernet
“Interference Nulling”
Alice
Bob
null
null
AP-1
OpenRF
AP-2
OpenRF
3 Mbps
3 Mbps
Buffering…
Buffering…
Notes: In effect, this technique uses the multiple antennas on the AP to re-direct the interfering beams away from the clients.

## Slide 19: OpenRF’s Goals
Ethernet
“Interference Nulling”
Alice
Bob
HD Quality!
HD Quality!
null
null
AP-1
OpenRF
AP-2
OpenRF
time
Alice
Bob
Alice
Bob
Alice
Alice
Bob
Bob
6 Mbps
6 Mbps
Notes: This enables AP-1 and AP-2 to transmit simultaneously and hence go back to 6 Mbps each.
Thus they can both enjoy HD quality videos.

## Slide 20: OpenRF’s Goals
Ethernet
Alice
null
null
AP-1
OpenRF
AP-2
OpenRF
“Beamforming”
3 Mbps
6 Mbps
beamform
Bob
Notes: But now let’s say Bob walks farther away from AP-2,
… so his throughput drops to 3 Mbps.
In this case, OpenRF can apply another technique “coherent beamforming” to maximize received signal power to Bob.

## Slide 21: OpenRF’s Goals
Ethernet
Alice
null
null
6 Mbps
AP-1
OpenRF
AP-2
OpenRF
6 Mbps
Bob
beamform
OpenRF must self-configure to network dynamism
Notes: Essentially this leverages the AP’s antennas to focus the beam and maximize received power at Bob.
In effect, this can push Bob’s rate back to its original 6 Mbps.
Hence, OpenRF must be able to apply the right set of MIMO techniques to self-configure to such dynamism in the network.

## Slide 22: OpenRF’s Architecture
Ethernet
Alice
AP-1
OpenRF
AP-2
OpenRF
null
null
Bob
Flow-id
Action
PHY
techniques
OpenRF Interface
Control Plane
Data Plane
Notes: So let’s see how OpenRF’s architecture achieves this goal.
At the heart of OpenRF is an interface that separates the data and control plane.
The interface operates over a (flowid, action) table much like OpenFlow. In an OpenFlow switch, the action refers to an output port along which a flow must be forwarded.
In contrast, an OpenRF action refers to the PHY techniques that an AP applies to a flow.

## Slide 23: OpenRF’s Architecture
Ethernet
Alice
AP-1
OpenRF
AP-2
OpenRF
null
null
Flow-id
Action
To:Bob
beamform @Bob
null @Alice
Bob
beamform
OpenRF Interface
Control Plane
Data Plane
Notes: For example, the control plane may ask AP-2 to beamform any packet to Bob, while nulling it at Alice.
The interface then feeds this information to the data plane….

## Slide 24: OpenRF’s Architecture
Ethernet
Alice
AP-1
OpenRF
AP-2
OpenRF
null
null
Bob
beamform
Flow-id
Action
To:Bob
beamform @Bob
null @Alice
OpenRF Interface
Control Plane
Data Plane
Notes: … which redirects the signal beam to apply these techniques.
In other words, an action in OpenRF refers to the spatial direction along which a signal must be forwarded.

## Slide 25: OpenRF’s Architecture
Ethernet
Alice
AP-1
OpenRF
AP-2
OpenRF
null
null
Bob
beamform
In OpenRF, action = spatial direction to forward signal
Flow-id
Action
To:Bob
beamform @Bob
null @Alice
OpenRF Interface
Control Plane
Data Plane
Notes: … which redirects the signal beam to apply these techniques.
In other words, an action in OpenRF refers to the spatial direction along which a signal must be forwarded.

## Slide 26: Software Defined MIMO Networks
APs collect channel states and send them to controller
Controller automatically figures out where to apply interference nulling, alignment , MU-MIMO and inform the APs
Prototype is compatible with the 802.11n/ac standards

## Slide 27: Video Application
OpenRF
802.11
Blue
Red
Blue
Red
Frame Delay (ms)
Frame Delay (ms)
Two clients watch video over VLC
Notes: Finally, we measure the impact of OpenRF for real applications.
We consider two clients streaming a HD video over VLC.
We compare the delays in the video for 802.11 and OpenRF.
Here are the results.
For 802.11, the delays remain low when the blue client is the only client in the network, but clearly begin to spike once the red client joins the network.
In contrast, the delays remain low for OpenRF even when both clients are streaming video at the same time.
Let’s look at how this translates to Bob’s actual video experience. We start with 802.11
(Play)
As you can see the video suffers from major glitches and stalls. Next let’s look at OpenRF.
(Play)
Clearly the video is of much better quality!

## Slide 28: Centimeter-Scale Localization
Today, RF-based localization has about one meter accuracy
Challenge: Multipath effects confuse the localization system
Solution: Use the multipath reflection pattern as a signature of the location

## Slide 29: Use Multipath Reflections
Power of Reflection
Spatial Angle (degree)
Reader
35o
35o

## Slide 30: Use Multipath Reflections
Power of Reflection
Spatial Angle (degree)
Reader
140o
140o

## Slide 31: Use Multipath Reflections
Power of Reflection
Spatial Angle (degree)
Reader
Can localize to within a few centimeters

## Slide 32: Works even with RFIDs
Battery-free stickers to tag any and every object

## Slide 33
No more customer checkout lines
RFIDs on goods

## Slide 34
No more customer checkout lines
RFIDs on Basket

## Slide 35
Red Pringles RFID
Shelf RFID
Basket RFID
Pringles
Basket
Shelf

## Slide 36
Red Pringles RFID
Basket RFID
Shelf RFID
Basket
Shelf
Pringles

## Slide 38: Smart Homes
RFID-tagged Laptop
RFID-tagged
Laptop Charger
RFID-tagged
Handbag

## Slide 39: Smart Homes
Reference RFIDs

## Slide 40: Smart Homes

## Slide 41: Smart Homes
Charger left behind!
RFIDs on the Door Frame

## Slide 42: Can your cellphone give you X-ray vision?

## Slide 43: WiVi: See through-walls with WiFi
WiFi signals traverse walls and reflect off objects
Challenge: reflections off the separating wall are 10,000x higher than off a human behind the wall
Solution: use two transmit antennas and one receive antenna; the two transmitted waves cancel each other for static objects but not animated objects
See video on YouTube
https://www.youtube.com/watch?v=uJkQzLjYBFI

## Slide 44: Securing Medical Devices
Medical implants and sensors are power limited
 Can’t have strong cryptography

## Slide 45
Notes: So here we have a off the shelf software radio which as we can see is connected to a laptop.
Next we have an implanted cadiac defibrillator on which we demonstarte the shock. Behind it is an oscilloscope which we use to monitor the implant.
Now let us send a command on the laptop to deliver the shock. The software radio is sending the signals and the laptop now says that the shock has been delivered.
Now on the oscilloscope, we see voltage spike confirming that the shock as been delivered.
We are going to repeat this experiment multiple times and focus on what’s really happening at the implant.
As we can see, the resistor on the implant starts burning. Clearly, this is not desirable inside a human body.

## Slide 46
Reader knows the jamming signal
subtract it
decode implant’s transmission
Deliver data to doctor
Implant’s signal
Reader
jams
Random Sum
Doesn’t know jamming signal
 can’t decode
Encryption on the Air
Encrypt using a random signal
Jamming signal acts as an analog one-time pad
How does the reader decrypt?
Can secure medical devices even if they have no encryption of weak encryption
Notes: Our solution is called encryption on the air.
So say we have an eavesdropper who is trying to snoop on the implant’s data.
In order to encrypt the implant’s transmissions, the reader is going to use a random signal.
So say this is the implant’s signal. The reader pciks a random signal and jams the implant’s transmission.
Now since the eavedropper does not know the jamming signal, it cannot decode the implant’s signal.
Thus, effectively, the random jamming signal acts as a one-time pad.
But how does the reader decrypt this signal?
Remember that the reader knows the random jamming signal because it is the one who generated it.
So, in principle, it can subtract the jamming signal and decode the implant’s transmission.
The reader then forwards the decrypted data to the health care professional.
So we want a wireless device that can transmit and receive simultaneously, which is a hard problem.

## Slide 47
All TV programs to your handheld device
Live broadcast of concerts and sports anywhere anytime
But today’s mobile video suffers glitches and stalls
Mobile Video Is the Killer App.
Notes: According to all predictions, Mobile video is the next killer application
[animate] We all want to watch TV programs on our handheld devices
[animate] watch live broadcast of concerts and sporting events, anywhere, anytime
[animate] The problem however is that today’s mobile video glitches and stalls.
Without a solution, it is unlikely mobile video will achieve its potnetial.

## Slide 48: Why Does Video Suffer Glitches and Stalls?
Video codecs, originally designed for DVD and CD
Assume no errors or drops
Wireless has high bit errors and packet drops
Today’s video has two isolated components
Video Glitches and Stalls
Wireless Physical Layer
Video Compression
Notes: But why does today’s mobile video glitch and stall?
[animate] Today’s video has two components that are designed in isolation from each other.
[animate] Specifically, it has a video codec which compresses the video.
It also has a wireless physical layer that encodes the bits to produce the transmitted signal
[animate] The problem however is that the video codec (i.e., MPEG4/H264 and its variants) was originally designed to store video on DVD and CDs. It does a great job on compression. BUT IT ASSUMES NO BIT ERRORS or packet drops.
It becomes very fragile in the presence of errors or drops.
[animate] the Wireless physical layer on the other hand suffers from bit errors and packet drops.
So, you take a video that assumes no error or packet drops and you put it on top of a channel that has drops and errors 
[animate] You get video glitches and stalls
[animate] That is you get a system that works perfectly when there are no residual errors after decoding. But even if there is only one bit error after decoding, it can result in an arbitrary amount of errors in the video.
[animate]

## Slide 49: Our Solution: SoftCast
Wireless Physical Layer
Video Compression
Joint code to compress and protect from channel errors
Pixel Values
Digital Signal
Optimizes video compression and channel coding together
Smooth degradation; No glitches or stalls
Code Is Linear
Small perturbation on channel
Small perturbation in pixel values
Notes: Softcast solves this problem
At a high level it works as follows:
[animate] instead of having two components one for compression and one for encoding the signal to transmit it on the channel,
[animate] Softcast has a single code that both compresses the video and protects it from errors as it is transmitted over the wireless channel.
[animate] SoftCast code however is special in that it makes the whole network stack with all of its layer act like a linear transform
Thus the least significant bits in pixels’ luminance get mapped into the least significant bits in the transmitted signal samples,
And the most significant bits in pixels’ luminance get mapped into the Most significant bits in the transmitted signal samples,
Hence, video shows a smooth performance and no glitches or stalls.
[animate] Moreover the code can maintain this smooth degradation while compressive the video.
[Animate] thus, when channel variations cause small perturbations in the signal samples, this translates into similarly small perturbations in the pixel luminance
[animate] and no cliff effect.
[animate] alone this is not sufficient

## Slide 50: The Sparse Fourier Transform

## Slide 51: The Fourier Transform Is Everywhere
Audio
Video
Medical Imaging
Radar
GPS
Sequencing
Oil exploration
Notes: FFT is widely used
Making improvement to the way we do FFT  improvement to large number of applications and domains.

## Slide 52: Computing the Discrete Fourier Transform
Naïve Algorithm O(n2)
In 1965, Cooley and Tukey introduced the FFT which computes the frequencies in O(n log n)
But … FFT is too slow for BIG Data problems
Can we design a sublinear Fourier algorithm?

## Slide 53: Idea: Leverage Sparsity
Often the Fourier Transform is dominated by a few peaks
Time Signal
Approximately Sparse Freqs.
Sparse FFT runs in sub-linear time on sparse data
Fastest Algorithm today
Top 10 Emerging Technologies -- Technology Review

## Slide 54: How Does the Sparse FFT Work?
Divide spectrum into a few buckets
f
Estimate the large coefficient in each non-empty bucket
1- Bucketize
2- Estimate
 Can ignore empty bucket

## Slide 55: Simulation Results
Chart: Run Time vs. Signal Sparsity (N= 222 ≈ 4 million)
| 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768 | 65536 | 100000 | 131072 | 262144
FFTW | 0.5542 | 0.5542 | 0.5542 | 0.5542 | 0.5542 | 0.5542 | 0.5542 | 0.5542 | 0.5542 | 0.5542 | 0.5542 | 0.5542 | 0.5542 | 0.5542
SFFT 3.0 | 0.0004877 | 0.00074713 | 0.0012342 | 0.0022569 | 0.0042448 | 0.0078418 | 0.014846 | 0.031898 | 0.066858 | 0.14312 | 0.33898 | 0.51541 | 0.73767 | 1.4832
FFTW
Sparse FFT

## Slide 56: 3D Photography Using Sparse FFT
Generate depth and perspective using a camera array
Images are correlated 4D frequencies are sparse
Goal: reduce the number of camera elements to enable implementation in a hand-held device
Solution: Camera images are correlated Use sparse FFT

## Slide 57: Results show that we can accurately reconstruct unsampled camera outputs

## Slide 58: Conclusion
Exciting opportunities in the wireless and mobile domains
  MegaMIMO brings 10x increase in data rates
  Centimeter-scale indoor localization
  The sparse FFT enables 3D imaging
  WiVi enables portable devices like cell-phones to track people through walls and closed rooms
http://groups.csail.mit.edu/netmit/wordpress/