## Slide 1: See Through Walls with Wi-Vi
6.888: Wireless Communication Systems
October 24, 2013

## Slide 2: Can your cellphone give you X-ray vision?

## Slide 3: Key Idea

## Slide 4: Challenges
Wall refection is 10,000x stronger than reflections coming from behind the wall
Tracking people from their reflections
Notes: The technical problem with the wall’s reflection is due to the limited dynamic range of the ADC (analog to digital converter). The dynamic range is the ratio of the strongest to the weakest signals that can be registered simultaneously
For an ADC with 10 effective number of bits, the ratio is about 4K < 10K.
Therefore, the wall’s reflection will saturate the ADC and prevent it from registering any signal coming from behind the wall.

## Slide 5: Applications
Police avoids ambush
Firefighters check for humans
Personal security
Gesture interface from behind a wall

## Slide 6: Wi-Vi: Small, Low-Power, Wi-Fi
Eliminate the wall’s reflection
Track people from reflections
Gesture-based interface
Implemented on software radios

## Slide 7: How Can We Eliminate the Wall’s Reflection?

## Slide 8
Idea: transmit two waves that cancel each other when they reflect off static objects but not moving objects
Wall is static
People tend
to move
disappears
detectable

## Slide 9: Eliminating the Wall’s Reflection
Transmit Antennas
Receive Antenna:
αx
x

## Slide 10: Eliminating the Wall’s Reflection
h2
h1
y = h1 x + h2αx
0
α = -h1 / h2
Receive Antenna:
αx
x
Notes: We estimate h1 and h2 using standard channel estimation techniques:
We transmit a signal x from first antenna alone, gets multiplied by h1 over the air, we get at the receive antenna y1=h1*x. We know x and we receive y1. so we can compute h1=y1/x
We stop transmitting from first antenna and transmit x from second antenna. It gets multiplied by h2 over the air. We can compute h2=y2/x
This is of 1 reflectors. What if have multiple reflectors? Wireless signals linearly combine. But, key thing to note is that our estimation of h1 did not assume 1 reflector. So, the technique really cancels out all static reflections.

## Slide 11: Eliminating All Static Reflections

## Slide 12: Eliminating All Static Reflections
y = h1 x + h2αx
Static objects (wall, furniture, etc.) have constant channels
y = h1 x + h2(- h1/ h2)x
0
People move, therefore their channels change
y = h1’ x + h2’(- h1/ h2)x
Not Zero
h2
h1
αx
x

## Slide 13: How Can We Track Using Reflections?

## Slide 14: Tracking Motion
Direction of reflection
θ
Antenna Array
RF source

## Slide 15: Tracking Motion
θ
Antenna Array
Direction of motion
At any point in time, we have a single measurement

## Slide 16: Tracking Motion
θ
Antenna Array
Direction of motion
θ
Direction
of motion

## Slide 17: Tracking Motion
θ
Antenna Array
Direction of motion
θ
Direction
of motion
Human motion emulates antenna array
Notes: We talked in class about the relationship between doppler shift, ISAR, SAR, and antenna arrays.
Doppler shift is change in carrier frequency due to motion. Recall siren example given in class.
f(doppler) = f(transmitted)*v/speed_of_wave. You can derive it by looking at what happens to the wavelengths
The summary of what we said:
For antenna arrays: MP(theta) = sum(A[k]*e^(-j2*pi*d/lambda*k*cos(theta))
  We don’t know d for our case, because person is moving, we assume some velocity v => d=vT where T is sampling rate
  Instead of taking A[k] from the different antenna array elements, we take h[k] which is the channel across time and treat it as an antenna array
  This gives us: MP(theta) = sum(h[k]*e^(-j2*pi*vT/lambda*k*cos(theta))
For doppler shift, it’s a frequency shift. To get frequency shift, typically do an FFT or any fourier transform
  The DFT of the channel is: H(f_doppler) = sum(h[k]*e^(j2*pi*T*f_doppler*k))
  Recall f_doppler = f(transmitted)*v/speed_of_wave = f*v/c (where c is speed of light because electromagnetic wave)
  Because lambda = c/f, we get: f_doppler = v/lambda
  This gives us: H(f_doppler) = sum(h[k]*e^(j2*pi*T*v/lambda*k)
This means that the only difference between Doppler and ISAR is the cosine theta. Because people tend to move at fairly constant speed indoors, this theta gives us an intuitive way to look at interpret motion, and we can start getting some understanding of whether someone is moving in a circle or straight line, etc.

## Slide 19: A Through-Wall Gesture Interface
Sending Commands with Gestures
Two simple gestures to represent bit ‘0’ and bit ‘1’
Can combine sequence of gestures to convey longer message

## Slide 20: Gesture Encoding
Bit ‘0’: step forward followed by step backward
Bit ‘1’: step backward followed by step forward
Step Backward
Step Forward

## Slide 21: Gesture Decoding
Bit ‘1’
Bit ‘0’
Matched Filter
Peak Detector
Gesture interface that works through walls and none-line-of-sight

## Slide 22: Implementation and Evaluation
USRP software radios:
  Wi-Fi signals: 2.4GHz, OFDM
  5MHz to enable real-time channel estimation
  10mW transmit power
Old and new buildings on MIT campus
Eight human subjects
  200 experiments

## Slide 23: Tracking Multiple Humans
One moving person is indicated by a single curvy line
Notes: In our experiments, remember that a single human appears as one bright curvy line.

## Slide 24: Tracking Multiple Humans
Number of distinct curves at the same time corresponds to the number of humans
Two Humans
Three Humans
Notes: The important thing to note is that when the different antenna arrays are super-imposed, the signal becomes much noisier.
We need a way to disentangle the signals from different reflectors (people).
One option: MUSIC algorithm allows disentangling independent sources
Problem with it: the reflections are all correlated because come from same source!
To deal with this, use smoothed music algorithm. It uses the fact that signals arriving from different directions are get shifted by different amounts in an antenna array

## Slide 25: Automatic Estimation: Number of People
Detected Actual | 0 | 1 | 2 | 3
0 | 100% | 0% | 0% | 0%
1 | 0% | 100% | 0% | 0%
2 | 0% | 0% | 85% | 15%
3 | 0% | 0% | 10% | 90%
Classification algorithm in the paper
Notes: Look at curve of 1 person, energy is concentrated in 1 place => variance is small.
More people, energy is spread out => variance increases
Use simple machine learning algorithm, train on set and test on another set.

## Slide 26: Current Status